Teeth Whitening Accelerator

Operation and Installation Manual

(M-66)

Catalogue

- Safety………………………………………………………………………3

- Assembly Instruction Illustration…………………………………………4

- Product Features……………………………………………………………7

- Product Specifications………………………………………………………7

- Content………………………………………………………………………8

- Operation……………………………………………………………………8

- Warranty……………………………………………………………………9

SAFETY

PLEASE NOTE：

Prior to installation and start-up of the unit,carefully read the instructions provided herein

As with all technical devices, the proper function and safe operation of this unit depend on

the users compliance with the safety recommendations presented in these operating

instructions.

▲CAUTION：It is important to observe the following precautions:Do not shine the light directly onto or toward unprotected gingival or skin.

▲CAUTION：Persons with a history of photosensitivity or who are using photosensitizing drugs should not be exposed to light from this unit.

▲CAUTION：This equipment is not suitable for use in the presence of jlammable anesthetic mixtures with air or nitrous oxide.

▲CAUTION：Plase do not look into emitted light by the machine when it is in use or it will hurt your eyes, plase be sure to wear gogglesl.

▲CAUTION：The angle of bend in use please do not exceed 90 degree, or easily broken elbow, It maybe cause noise in future.

Assembly Instruction Illustration (一)

Warning: When this screw is loose, the spring will be come out.

Assembly Instruction Illustration (二)

Host Button Manual

Remote Control Manual

Product Features

- High efficiency goose pipe design, adjust angle at random, convenient for use.

- Combination of high power BLUE led.

- Tunable bleaching time with microprocessor-controlled timer presets.

- Digital indicator with audio feedback.

- Smart auto-select power: 100~240V 50/60 Hz for global use.

- High speed Multi-Arch teeth whitening system.

- Small base size design, suitable use in dental clinic.

- Hight uniformity of light output.

- Hight sensitive infrared remote control setting function.

- Enclosed disposible sheath, prevent cross-infection,clean and convenient,let patient feel relieved.

Product Sepcifications

- Broad Spectrum: 420nm~472.5nm(Host Lamps)

- Light Output Power: Up to 2000 mW/cm

- 100-240V,50/60Hz

- Weight 6.74Kg

- Max. Working Radius:50cm

- Hiht Uniformity of light output:

| Distance beween teeth and Illuminator(mm) | Uniformity |
| --- | --- |
| 1mm | Above80% |
| 3mm | Above80% |
| 5mm | Above80% |
| 10mm | Above80% |

TEETH

Content

| M-66 | 1 pcs |
| --- | --- |
| M-66 Foot stool | 1 set |
| 12V adaptor | 1 pcs |
| Power cable | 1 pcs |
| Glass | 2 pcs |
| Lamp shade | 10 pcs |
| Remote control | 1 pcs |
| Mouth | 1 pcs |
| Assembly Tool | 1 set |
| Disk with Manual | 1 pcs |

Operation

Turn On The Teeth Whitening Accelerator

A)Plug in the teeth whitening Accelerator.

B)Turn on the power switch

Teeth Whitening DC power plug

Warning:

We fixed safe fuse in it, if the current overloaded,it will cut off immediately, when you change new fuse,everything will work smoothly as usual.

Operating The Teeth Whitening Accelerator

A) : Turn on/off the light by pressing the START/STOP button.

B) : Stop the time counting and emitting light by pressing the Pause button. The remaining whitening time will sparkle on the digital indicator. Press the Pause button again,light will emit and time will count continually.

C) : Use UP or Down button to set whitening time.5 minute counting with memory, the longest whitening time is 30 minutes each cycle.

1.Sound Warning

A)After starting, the machine will beep each minute.

B)You will hear three beeps after finished.

2.Cooling Setting

A)To guarantee all leds could work at the normal temperatre when whitening process, we fix a high efficiency and quite fan to expel heb.

B)Besides, we built-in smart temperature protection, when it meets high temperature will shut down power utomatically, after cooling,all can work properly.

3.Liability

It is responsible for the effects on safety, reliability and performanceof this product only if:

- The electrical installation of the relevant room complies with therequirements.

- The equipment is used in accordance with these instructions for use.

Maintenance Illustration for Product

Thanks for you have bought our company products, For ensuring our company can offer top quality after-sell to you, Now, we shall tell you following illustration for maintenance to guarrantee your right：

一．Maintainable condition of product

1.The product, which you have bought, is one year for maintenance, In this term, you can request sellers or our company to seek counsel and maintain about the product if your product has some questions.

2.Following situations will be removed at the serviced scope of analyzer, and we shall get costs(Standard of charge is contained repaired cost add to fee of replaced spares add to fee of traffic or post)

1）Customer-self is used unsuitable, or has not accorded to the user manual.

2）After our products have broken downed, but customer-self have changed and repaired, or with any maintained stations that haven’t been our company authorizing have maintained relation

3）For installation or moving and so on reasion, which is caused man-made damage or hitch.

4）Accident for unexpected disaster(eg: fire,water,seism,thunderstruck,gas-explode and so on)

3．The analyzer has passed by stipulations of the quality managements to be inspected, but we can’t remove the caused factors for tansport.Once your analyzer has hitch, please get in touch with sellers or our company with your maintenance, and you will get service.

4.Please call：_+86-755-33813513_If you can’t get better service

二．Please fill in following items(You must fill in which have noted*)：

﹡Type：_______            ___ ﹡Item No.：____          ________

Term of maintenance：ONE YEAR

Note: The term of maintanance begin-data is according to buy-data of the analyzer

Maintenance NO.：_____               _____

﹡Name of company：___________________________________

﹡Zip/Post：_________________________    __________

﹡Tell：________   ____ ﹡Fax： __   _________

Seller’s name：___________________________________

﹡Buy-data：___________ ﹡Invoice No.：____   ______

| Reason of hitch | Method of maintenance,change shares | Date of maintenance |
| --- | --- | --- |

# Text boxes

Time display

IR

Power

Pause/continue

Time setting (Down)

Start / Stop

Time setting (up)

Pause/continue

Power

Time setting (Down)

Start / Stop

Time setting (up)